## Slide 1: Project Hi-ball In Conjunction With: Nasa space Grant Consortium Embry-Riddle Aeronautical university
Project Members:
Bryce Fox
Jessica Avitia
Sara Daniella Eriksson
Mary Begay
ASGC Symposium April 18, 2009 at
Arizona State University
Mentors:
Dr. Ron Madler
Jack Crabtree

## Slide 2: Presentation Overview
Project Hi-Ball Description and Overview
2008-2009 Year-Long Goals
Accomplishments and Research Progress
Long-Term and Future Goals
Acknowledgements and Audience Questions

## Slide 3: Project Hi-Ball Description and Overview
Hi-Ball: High Altitude, Scientific/Weather Ballooning
The Team was created to support and advance the scientific and weather ballooning community on the Embry-Riddle Aeronautical University Prescott Campus (ERAUPC).
The Team’s work and research includes, but is not limited to:
Goals directly involving implementation of scientific payloads in relation to high altitude/scientific ballooning
Projects involving the experimental aspects of engineering, focusing on the integration of systems having to do with high altitude atmospheric flights and future space satellite missions
Launching, tracking and recovery of scientific payloads for Hi-Ball and other ERAUPC scientific ballooning groups

## Slide 4: 2008-2009 Year-Long Goals
Design, build, test and fly a reliable GPS Tracking box that can
be updated in the future to include more scientific payload.
Research ways to implement a cut-down or release mechanism
to enable the team to abort a mission after the payload has
left the ground, (mid-flight).
Support the HASP (High Altitude Student Platform) team on
the ERAUPC and Pima Community College (PCC)by designing,
building and testing a structure to withstand the extreme
environment at an altitude of 36 km, for up to 48 hours.
Support a Senior Detail Design Class on the Embry-Riddle Prescott
campus, by designing, building and successfully implementing a
release mechanism for a payload attached to a weather balloon.

## Slide 5: Accomplishments/Research Progress
Detail Design Cut-Down Mechanism
Research was conducted on how to best fit our requirements
while at the same time allowing for future modification to
accommodate our goals
- Reusable design, which can be easily modified/changed for future improvements on the design for all future flights as an abort system
Design specifications settled on, and mechanism assembled
- Nickel-Chrome wire was used to burn an attachment rope to drop payload
- Picaxe 18X chip used for ease of programming, reusability and weight
- Hope HM-TR transceivers used for communication with the device
from the ground, using hyper terminal
- Assembled on a prototype board, with required circuit layouts
- Temporary structure to be used for the first flight test, with plans to construct a permanent structure from E-Glass fiber
Design tested positively, and implemented for intended purpose

## Slide 6: Accomplishments/Research Progress cont.
GPS Tracker Payload
Basic internal components reused from a previous tracker box
New structure designed and built using E-Glass Fiber
Launch and successful recovery of the payload for first flight test
Successful cold chamber testing
Design created in Catia to meet size requirements (15x15x30 [cm])
and to model the required insulation and layout
Structure to be deconstructed into two halves, one for each team,
to be reassembled at final integration
Built an Engineering prototype for mock-up of internal systems
by both the ERAUPC and PCC teams, excluding part of the
thermal insulation (thick foil to be added to the flight model)
- E-glass fiber with a .5” high-density foam core was used for
the best thermal insulation properties
Final flight model to be built in the early weeks of summer with
temperature testing to follow soon afterwards to ensure required
thermal insulation requirements are attained
HASP Structure:

## Slide 7: Long-Term/Future Goals
The team has several long-term research and project goals.
Research involving the creation of a constant-altitude balloon
platform to enable state-wide emergency radio communication
ability or to make ground observations for periods of 48-72 hours.
Implementation of both physics and meteorology experiments in
a high-altitude environment, to be developed in conjunction with
both the physics and meteorology departments on ERAUPC.
Creation of a truly student run, sustainable, scientific/weather ballooning
community on ERAUPC.
Long-term development of the infrastructure and knowledge-base
required for the eventual development of a full-size Embry-Riddle
satellite

## Slide 8: Acknowledgements
Special Thanks Goes to:
Dr. Ron Madler
Jack Crabtree
Dr. John Nafziger
Chris Smith
And All Other Partners of the Arizona Space Grant Consortium
Questions ??