## Slide 1: University of Arizona ASCEND!
Team Members:
Tiara Cottam, Andrew Dotson,
Michael Palmer, Kyle Stephens
Team Mentor:
Mike Borden

## Slide 2: Objectives
Fall Semester:
  Take high quality panoramic images of the earth
  Use a timing circuit to automate and synchronize cameras
Spring Semester:
  Take the solar spectrum at different altitudes
  Learn about cost effective solar spectroscopy

## Slide 3: Payload: Fall Semester
Four Sony Cybershot DSC-W290 (12 MP) cameras
FOV of one camera: 35°
Total panoramic FOV: 135°
Timing circuit was used to sync cameras
Timing interval: 1 picture every 10 seconds

## Slide 4: Results: Fall Semester
Cameras worked up until about 40,000 ft when timing circuit failed
200 pictures per camera were obtained with about 40% able to be merged

## Slide 5: Spectrometer Temperature
Chart: Spectrometer Temperature for 3/27/10 ASCEND! Launch
Temperatures ranged from 60°F to 90°F
Spectrometer temperature affects the magnitude of each spectrum collected
Temperature data was to be used to calibrate raw data
Balloon Burst
Landing

## Slide 6: Payload: Spring Semester
Spectrometer
350nm-1000nm
0.2 second exposure
Data taken every 5 seconds
Laptop
Asus EeePC
Removed monitor to conserve power and weight
HOBO Data Loggers
4 Channel HOBO connected to a thermistor by spectrometer
3-axis data logger used to track payload position

## Slide 7: Post Launch Data Reduction
Assumptions
  Higher Magnitudes means Fiber Pointed at Sun
  Good Spectrums taken from High Magnitudes
  Altitude Data matched to Spectrum timestamp
Data
  1084 total spectrums
  3,440 Data Points per spectrum
  Spectrums logged every 5 seconds
  Converted from log file to Excel Workbook
Normalized Data
  Reduced statistical errors in our measured data

## Slide 8: Results: Spring Semester
Chart: Solar Spectrum (Altitude: 15,223 ft)
H2O present

## Slide 9: Results: Spring Semester
Chart: Solar Spectrum (Altitude: 40,155 ft)

## Slide 10: Results: Spring Semester
Chart: Solar Spectrum (Altitude: 65,965 ft)

## Slide 11: Results: Spring Semester
Chart: Solar Spectrum (Altitude: 83,041 ft)
H2O not present
O2 not present

## Slide 12: Thank You
Acknowledgements:
  Arizona Near Space Research
  Arizona Space Grant Consortium
  Susan Brew
  Mike Borden