## Slide 1: Aerospike and Conventional Bell-Shaped Nozzles: A Numerical Comparison of High-Powered Sounding Rocket Flight Profiles
Presenter: Peter Renslow
Advisors: James K. Villarreal and Steven Shark

## Slide 2: Rocket Nozzle Theory
Rocket thrust is dependant on two things:
  The mass flow rate of propellant being ejected from the nozzle
  The difference in ambient air pressure and nozzle exit pressure
The Thrust Equation:
Mass flow rate component
Pressure Differential Component
Thrust is maximized when the nozzle exit pressure equals the ambient pressure

## Slide 3: Bell Nozzles

## Slide 4: Bell Nozzle Expansion Modes
The traditional bell-shaped nozzle has a fixed geometry that is only able to expand exhaust gas to one fixed pressure

## Slide 5: Aerospike Nozzles

## Slide 6: Aerospike Nozzle Expansion Modes
Pa > Pdesign
Pa = Pdesign
Pa < Pdesign
The aerospike nozzle’s expansion section is open to ambient atmosphere
The aerospike nozzle expands the exhaust gas to ambient air pressure at all altitudes below a design altitude

## Slide 7: The Aerospike Advantage
Because atmospheric pressure decreases with altitude, sustained perfect nozzle expansion during flight within the atmosphere results in:
  Increased Thrust, Total Impulse, Specific Impulse
  This results in increased apogee altitude or payload weight
In order to quantify the advantage of using an aerospike nozzle, a numeric model was created to simulate terrestrial rocket flights

## Slide 8: The Numerical Model
Uses basic Newtonian kinematics and aerodynamic drag
Based on a arbitrary rocket built around the STAR 27 Apogee Motor
  The expansion ratio and burn time is varied to investigate its effect
Assumptions:
  Coefficient of Drag = 0.2
  Exhaust gas ratio of specific heats γ = 1.4
  No flow losses in either nozzle; aerospike operation is ideal
  Rocket flight is straight up and straight down
  Stable weather conditions

## Slide 9: Results: Altitude vs. Time Plots
Expansion Ratio = 2
Expansion Ratio = 25

## Slide 10: Results: Tables
Expansion Ratio = 2
Expansion Ratio = 25

## Slide 11: Results: Doubled Burn Time
Expansion Ratio = 5, Burn Time = 34.35
Expansion Ratio = 5, Burn Time = 68.7 sec

## Slide 12: Results: Doubled Burn Time
Expansion Ratio = 5, Burn Time = 34.35
Expansion Ratio = 5, Burn Time = 68.7 sec

## Slide 13: Conclusions
The increase in performance due to an aerospike nozzle depends heavily on two factors
  The expansion ratio of the bell nozzle being compared to the aerospike nozzle
    There is an optimum expansion ratio for the bell nozzle that maximizes its performance, which still falls short of the aerospike nozzle performance
  The burn time of the rocket motor
    The longer the burn time, the greater the performance advantage of the aerospike nozzle
    Doubling the burn time increases the aerospike performance advantage by a factor of 10

## Slide 14: Conclusions
The advantage of the aerospike is fairly marginal at the chosen burn times when compared to the optimum bell nozzle expansion ratio
It may be difficult to justify the time and cost necessary to bring the aerospike to operational status
Suggested applications:
  Extremely long (> 2mins) burn times
  Extremely large expansion ratios (> 100) for use in space, where pa → 0

## Slide 15: Future Work
Daedalus Astronautics @ ASU is currently conducting research on aerospike nozzles, and plans to incorporate them into high-powered sounding rockets
  The numerical model will be used to predict the rocket’s performance
  One big hurdle: achieving long burn times in student-build rocket motors without structural failure

## Slide 16: Questions?