## Slide 1: Active Flow Control over an Airfoil with Nanosecond Pulse Driven DBD Plasma Actuators
Keith Sangston
Undergraduate Research Intern
Jesse Little
Assistant Professor, Department of Aerospace
and Mechanical Engineering
The University of Arizona
April 21, 2012

## Slide 2: Problem
At large angles of attack, the wings of an aircraft will experience stall. This results in…
  Airflow separation
  Reduced lift
  Increased drag
  Decreased aircraft control
2

## Slide 3: Nanosecond DBD plasma actuators
Without DBD Actuation
With DBD Actuation
Reduced airflow
separation
Increases lift
Increases aircraft control
Decreases drag
Decreases airflow separation
Plasma actuation…
3

## Slide 4: Goal
Better understand the physics behind the use of nanosecond pulse driven dielectric barrier discharge (DBD) plasma actuators to control the airflow around an airfoil
Dominant mechanism believed to drive phenomenon:
  Thermal energy transfer from discharge
4

## Slide 5: Airfoil construction - Design
MAJOR PARTS:
Molds
Polyurethane casting resin
Wind tunnel mount
Endplates
Designed in SolidWorks (Computer-Aided Design program)
1
2
3
4
5

## Slide 6: Airfoil construction - Manufacture
Mount & Support
(Metalworking)
Endplates
(CNC)
Molds
(Router)
Casting
(Polyurethane)
6

## Slide 7: DBD plasma actuator
High voltage electrode
Covered, grounded electrode
Kapton tape dielectric barrier
1
2
3
Dielectric:
Insulator that may be polarized by an electric field
7

## Slide 8: Electrical signal input
SOURCE: Rob Dawson, Graduate Student, University of Arizona
Peak ≈ 12 kV
Time of rise and fall ≈ 100 ns
8

## Slide 9: Thermal mechanism - Shockwave
SOURCE: Rob Dawson, Graduate Student,
University of Arizona
Schlieren imaging (0-20 µs)
Schlieren imaging is used to visualize flows of fluids due to varying densities
Rapid localized heating
Shockwave propagates outward
9

## Slide 10: Flow visualization
Method: Tufts (unwound yarn)
Longer exposure
shows movement
of tufts, which
indicates stall
Actuation: OFF
10

## Slide 11: Flow visualization
Plasma forms
On leading edge
Tufts laying flat
11

## Slide 12: Flow visualization: Actuation ON
Angle of Attack:13°
Frequency: 650 Hz
Voltage:500 V
Angle of Attack:15°
Frequency: 1250 Hz
Voltage:500 V
12

## Slide 13: Flow visualization
Angle of Attack:
13°
Frequency:
650 Hz
Voltage:
500 V
13

## Slide 14: Concluding remarks
Results:
Tufts going flat during actuation illustrate airflow reattachment
Driving frequency dependent on angle of attack
DBD plasma actuation positively affects airfoil performance
Potential benefits of DBD actuation:
Increased safety
Lighter, more efficient aircraft
Require relatively low power
Other airflow control applications
14

## Slide 15: Future steps
Force measurements
  Lift, drag, pitching moment
  Quantify effects of DBD plasma actuation
Experimentation with resistors
  Changes rise time of signal
  Varies thermal effects of actuation
15

## Slide 16
Thank you for your attention!
Special thanks:
  Susan Brew & Barron Orr
  Jesse Little
  Intern advisors
16

## Slide 17: Electrical setup
Oscilloscope
Function generator
120V-1A DC Power supply
Controller unit
Main unit
DC Power supply
1
2
3
4
5
6
17

## Slide 18: Airfoil construction
NACA 0015 airfoil chosen
Chord
t
Chord is distance between leading edge and trailing edge
‘00’ = Symmetric shape
‘15’ = Max thickness, t, is 15% of chord length
18