## Slide 1: Superconductive Magnetoresistive Random-Access Memory (JMRAM)
By
Charles Nathan Cardinell
Mentor
Nathan Newman

## Slide 2: Objective
To create a RAM that requires very little power
Resistive to Radiation Damage
Fast Switching

## Slide 3: Memory Comparision
 | FLASH | DRAM | SRAM | JMRAM (projected)
Cell Size (μm^2) | 0.04 | 0.03 | 0.3 | <1.25
Read Time (ns) | 10 - 50 | 10 | 1 | <5
Write Time | .1 - 100 ms | 10 ns | 1 ns | <5 ns
Write Energy per Bit | 10 nJ | 5 pJ (Requires Refresh) | 5 pJ | 4 - 10 pJ
Endurance (read/write) | 10^15/10^5 | 10^15 | 10^15 | 10^15
Non-Volatillitile | Yes | No | No | Yes
JMRAM has a faster read/write time
JMRAM is low power
JRAM has high endurance

## Slide 4: Review of Magnetoresistive Random-Access Memory (MRAM)
Non-Volatile
Data stored as a magnetic element

## Slide 5: Review of Superconductive Magnetoresistive Random-Access Memory (JMRAM)
Uses Josephson Junctions
Faster then Normal MRAMs

## Slide 6: Growth of the JMRAM
(Ultra-High Vacuum) UHV chamber
4 guns and targets
Large temperature range
Vacuum to 10-9 Torr
Sapphire and Silica substrates

## Slide 7: Types of Devices
Shadow Mask
Advantages
  Cheap
  Fast
Disadvantages
  Larger Device Area
  Poorer Quality Films
  Less Consistant
Processed
Advantages
  Multiple Device Sizes
  Multiple Devices
  Better Quality Films
  Less Pin Holes
Disadvantage
  Expensive
  More Chances for a mistake to occur

## Slide 8: Processing of the JMRAM
Step #1: Reduced Working Area Etch
Step #2: Junction Definition Etch
Step #3: Silica Dioxide Deposition
Step #4: Via Etch
Step #5: Metal Liftoff

## Slide 9: Measuring the JMRAM
Done in a shielded room
Wide range of temperatures and magnetic fields
Digital Systems Used

## Slide 10: Results
Chart: NHP4-1 at 5.3K, Ic=34uA, Rn=8.3 Ohm.

## Slide 11: Conclusions
JMRAM has the possibility to be used in a wide range of areas such as
Satellites
Banks
Search Engines
Databases

## Slide 12: Thank you
Questions?