## Slide 1: Ice Crystal Parameterizations in Arctic Cirrus – Towards a Better Representation in Global Climate Models and Aircraft Icing Potential Studies
Victoria A. Walker
Embry-Riddle Aeronautical University

## Slide 2: Statement of Purpose
Study the microphysical properties of arctic cirrus
Investigate possible correlations between aircraft icing and ice crystal SDs

## Slide 3: Cirrus and Global Climate Models (GCMs)
Cirrus feedbacks affect model output of T, radiative forcing, albedo, and heat flux.
Cloud properties a function of IWC and SDs.
  Radiative properties depend on T and SDs.
Not thoroughly studied at high latitudes.

## Slide 4: Aircraft Icing: Ice- and Mixed- Phase Clouds
FAA certifies clouds containing only SLDs.
Canadian Freezing Drizzle Experiment (CFDE)
  Non-classically formed SLDs ~ 80%
  Ice- or mixed-phase clouds ~ 50%
Non-classically formed SLDs have not been thoroughly studied.

## Slide 5: Optical Sampling Instruments: FSSP (left) and 2DC (right)

## Slide 6: DoE – ARM Research Flights
Flight 1 | Flight II | Flight III
666 | 366 | 210
After Criteria for Statistical Relevance [5 small mode, 4 large mode] |  | 
533 | 320 | 161
Oliktok Mobile Operations Base
3 Flights: 30 Oct 13, 3 Nov 13, 7 Nov 13

## Slide 7: Gamma Distribution: No, λ, v
 | No | λ | v
Average | 1.65 | 3.89 | 2.84
Flight 1 | 1.25 | 3.76 | 2.33
Flight 2 | 1.85 | 3.96 | 2.91
Flight 3 | 1.73 | 3.85 | 2.90

## Slide 11: Arctic Cirrus – Variation with T

## Slide 12: SD Variation with T: Tropical (left) and Mid-Latitude (right)

## Slide 13: Implications for Aircraft Icing
Aircraft icing during aggregation, accretion, and mixed-accretion events must be the focus of further study.
Particle interactions with aircraft, such as collapse, erosion, and structural breakup upon impact, should be thoroughly investigated.

## Slide 14: Conclusions
Arctic dataset is monomodal compared to tropical and mid-latitude datasets.
  Points to formation mechanisms at various latitudes.
Arctic cirrus may be linked to non-classical formation of SLDs.
Aircraft icing certification can only be achieved through an understanding of both ice- and mixed-phase cloud microphysics.

## Slide 15: Questions?
Image courtesy of http://onthickice.blogspot.com/

## Slide 17: Flight I: Synoptic Situation

## Slide 18: Flight II: Synoptic Situation

## Slide 19: Flight III: Synoptic Situation

## Slide 20: Formation Habits – Aspect Ratio