## Slide 1: Understanding the Shortcomings of CFD in Predicting High Lift Configurations
Ciara Thompson
Embry- Riddle Aeronautical University

## Slide 2: Purpose
Background
  2nd AIAA High Lift Prediction Workshop
  Assess the prediction capabilities of current CFD Technology
  Validate CFD results by comparing to wind tunnel experiments
  Compare CFD surface flow images to wind tunnel oil flow visualization images
Overview
  Experiment
  CFD
  Experimental and CFD Data Comparison
  Discussion
  Further Work
  Acknowledgments
  Q &A

## Slide 3: Model
KH3Y geometry
DLR-F11 model
EUROLIFT Project

## Slide 4: Experiment
Conditions
  Low speed wind tunnel test with an operating range of 60m/s
  Reynolds number 1.35e6
  Mach number of 0.175
Data Analyzed
  Oil flow visualization

## Slide 5: CFD
Cray XE6
  1024 compute cores
  24 hours of wall-clock time to converge
  7GB per file
OVERFLOW 2.2e
  Reynolds-Averaged Navier-Stokes solver by Pieter Buning, NASA Langley
  Structured Cartesian grid-69 million grid points
Solver settings
  Spalart-Allmaras
  AOA-7,18.5 and 21 degrees
    1 equation turbulence model
http://www.cray.com

## Slide 6: CFD Post Processing Procedure
Processed Data Provided by Dr. Earl P.N. Duque
Computing Power
  6 core AMD Phenom ΙΙ Processor
  16GB memory
FieldView 14
  Created surface streamlines using surface flow tool
  CFD Surface flow tool mimics oil flow visualization
Challenges
  Slow

## Slide 7: CFD Post Processing Results
Configuration 2
Configuration 4
Configuration 5
α=18.5̊
α=7̊
α=21̊
α=7̊
α=7̊
α=18.5̊
α=18.5̊
α=21̊
α=21̊

## Slide 8: Experimental and CFD Data Comparison
Alpha: 7 degrees
Color Code
Pink – Separation
Green - Surface flow lines
Blue Lines- Reattachment
Reattachment lines
α=7̊
α=7̊
CFD-Streamlines
Experiment -Oil Flow Visualization
8

## Slide 9: Experimental and CFD Data Comparison
α=7̊
α=7̊
CFD
Experiment
Separation lines
9

## Slide 10: Experimental and CFD Data Comparison
Alpha: 18.5 degrees
Color Code
Pink – Separation
Green - Surface flow lines
Blue Lines- Reattachment
Reattachment lines
Separation Bubble
α=18.5̊
α=18.5̊
CFD-Streamlines
Experiment -Oil Flow Visualization
10

## Slide 11: Experimental and CFD Data Comparison
Alpha: 21 degrees
Reattachment lines
Separation Bubble
Color Code
Pink – Separation
Green - Surface flow lines
Blue Lines- Reattachment
α=21̊
α=21̊
Experiment -Oil Flow Visualization
CFD-Streamlines
11

## Slide 12: Shear Stress: Configuration 5
α=21̊
α=18.5̊
α=7̊

## Slide 13: Experimental and CFD Data Comparison
Major Inconsistency
α=21̊
α=18.5̊
α=18.5̊
CFD
Experiment

## Slide 14: Experimental and CFD Data Comparison
α=21̊
α=21̊
CFD
Experiment

## Slide 15: Discussion
The results showed inconsistency in flow at higher angles of attack
Inconsistency may be a result of
  CFD physical models
  Wind tunnel errors

## Slide 16: Future Work
Compare surface flow of configurations 2,4 and 5
Compare pressure distribution of configurations 2, 4 and 5
Determine the causes of inconsistency between experimental data and CFD data

## Slide 17: Acknowledgments
CFD images were created using FieldView as provided by Intelligent Light through its University Partners Program
Simulations were performed by Dr. Earl P.N. Duque, Manager of Applied Research, Intelligent Light
NASA Space Grant
Faculty Advisor Dr. Shigeo Hayashibara

## Slide 19: Q&A

## Slide 20: Appendix

## Slide 21: References
Rudnik, R., Huber, K., Melber-Wilkending, S. “EUROLIFT Test Case Description for the 2nd High Lift Prediction Workshop”, AIAA 2012-2924, 2012
Nichols,R., Bunning,P., “User’s Manual for Overflow 2.2”, August 2010
Intelligent Light, FieldVIew 14, Software Package, Ver. 14, Rutherford, NJ
Christopher, R., “2nd AIAA CFD High Lift Prediction Workshop (HiLiftPW-2)”, NASA [http://hiliftpw.larc.nasa.gov/]
  All experimental results shown here were obtained from AIAA 2012-2924

## Slide 22: CFD- Code
OVERFLOW 2.2e
  This code is a finite difference mesh and solver
  It is a three dimensional time marching implicit Navier-Stokes code which can also be used for two-dimensional or axisymmetric mode
  The mesh is a structured grid system which consists of an overset of Cartesian grids to develop the desired model
  The model was meshed with a medium grid

## Slide 23: AIAA High Lift Prediction Workshop (Background)
The aim of the High –Lift PW was to assess the prediction capabilities of current CFD technology and to enhance CFD prediction capability for high lift configurations
The 2nd workshop was based on an experiment conducted under the German Aerospace Center for the European project EUROLIFT
The experiment was based on a typical geometry of a commercial high lift aircraft developed for the project and defined as the KH3Y geometry. The model was developed by the German Aerospace Center and denominated as the DLR-F11
The experiment was conducted in the low speed wind tunnel of Airbus in Bremen, Germany and in the high speed European
Transonic Wind tunnel
AIAA 2012-2924

## Slide 24: Experiment
Model
  The experimental model consists of a fuselage, and wing consisting of the following components: leading edge slat, and trailing edge Fowler flap
  Two configurations were developed
    Landing Configuration
    Take off Configuration
  The dimensions of the model are as follows
Half Span, s [m] | 1.4
Wing reference area, A/2 [m2] | 0.41913
Reference chord | 0.34709
Aspect Ratio | 9.353
Taper Ratio | 0.3
¼ chord sweep | 30
Fuselage length | 3.077
http://hiliftpw.larc.nasa.gov/

## Slide 25: CFD: Solver Settings
Turbulence model
  Spalart-Allmaras
    1 equation turbulence model derived using empirical relationships, dimensional analysis and Galilean invariance
    Fast and numerically stable turbulence model suitable of shear layers and boundary layers
  Mathematical description the turbulence model
    The mathematical model describes the production and dissipation of the turbulence