## Slide 1: Multi-Goal Path Planning Based on the Generalized Traveling Salesman Problem with Neighborhoods
by Kevin Vicencio
Aerospace and Mechanical Engineering Department
Embry–Riddle Aeronautical University
NASA Space Grant Symposium
April 11-12, 2014

## Slide 2: Motivation
Objective: Path length for redundant robotic systems.
Bridge inspection scenario
Rescue mission scenario
Travelling Salesman Problem (TSP):
Minimize tour length given a set of nodes
Widely Researched
Limitation: node location fixed

## Slide 3: Problem Dimension
TSP with Neighborhoods (TSPN):
Neighborhood: Node can move within a given domain
Determine optimal sequence and optimal configuration
Limitation: Cannot account for non-connected neighborhoods
Generalized TSPN (GTSPN):
Neighborhood Set: Node can be located in different regions
Disconnected neighborhoods can be modeled using smaller convex regions

## Slide 4: MIDP Formulation of GTSPN
Minimize:
Subject to:
(1)
Assignment Problem
(2)
DFJ Subtour Elimination
(3)
Neighborhood Set
(4)
(5)
Domain

## Slide 5: Neighborhoods
The used constraints (4) are:
ellipsoids: given symmetric positive definite matrices and vectors , center of the ellipsoid
polyhedra: given matrices and vectors
hybrid (multi-shaped): combination of rotated ellipsoids and polyhedra

## Slide 6: Hybrid Random-Key Genetic Algorithm
Genetic Algorithm:
Numerically obtain minimum
Function to be minimized: Distance
Utilize Natural Selection Techniques
  Crossover Operator
  Heuristics
Chromosome Interpretation:
  Sequence: Random-Key
  Neighborhood: Index
HRKGA Convergence History
Objective Value (m)
Generation

## Slide 7: Numerical Simulation Results
Alternative Crossover Investigation
Arithmetic Average Crossover Operator
  Offspring is arithmetic average of parents
  Mutates Index of neighborhood set
  HRKGA using Arithmetic Average operator is consistent within ±0.09% when determining tour
Uniform Crossover Operator
  Generate set of n uniformly, distributed random numbers
    If i-th element greater than a given threshold offspring inherits i-th gene of first parent.
    Otherwise, the offspring inherits the i-th gene of the second parent
  HRKGA using Uniform Operator is consistent within ±0.56% when determining tour
  On average HRKGA using Uniform Operator produces results:
    1.602% more cost effective
    0.920% less CPU Time
Average vs. Uniform

## Slide 8: Numerical Simulation Results
HRKGA Performance Evaluation on Randomly Generated GTSPN Instances
Evaluated using Uniform Crossover Operator
Number of neighborhoods per set: 6
40 Randomly generated instances
  Number of neighborhoods per set: 30,35,40,45,50
    Generated in: and
  HRKGA executed 15 times for each instance
Consistency when determining a tour:
  : ±0.59%
  : ±0.27%

## Slide 9: Near-Optimal Tours for GTSPN Instances
Random GTSPN Instance: , m = 6, n = 50

## Slide 10: Practical GTSPN Instance

## Slide 11: Future work
Algorithm:
Incorporate Dynamic Constraints
Incorporate Obstacle Avoidance
Physical Systems:
Implement Genetic Algorithm on multi-rotor vehicle
Optimize energy consumption

## Slide 12: Acknowledgment
Embry–Riddle Aeronautical University:
Dr. Iacopo Gentilini
Dr. Gary Yale
IBM Academic Initiative