## Slide 1: Analysis of Winglets for Low Reynolds UAV Flight Regimes
Aaron C. Pigott
Embry-Riddle Aeronautical University

## Slide 2: Introduction and Overview
Introduction
  Goal: Optimization of winglet sweep using STAR-CCM+
Overview
  Boeing AerosPACE
  UAV Design
  Why Winglets?
  Winglet Design
  The Mesh
  The Physics
  Results
  Conclusion

## Slide 3: Boeing AerosPACE
Collaborative senior design project with Boeing, Brigham Young University, Embry-Riddle Aeronautical University, Georgia Institute of Technology, Purdue University, and Tuskegee University
Objective: Successfully collaborate and design a hand-launchable Search and Rescue UAV
Winglet Analysis performed on Boeing AerosPACE UAV

## Slide 4: UAV Design
Length: 58.5 in.
Span: 92.8 in.
AR: 9
Main Wing Chord: 11.4 in

## Slide 5: Why Winglets?
Wingtip vortices cause induced drag
Induced drag reduces aircraft range and endurance
Winglets minimize wingtip vortices

## Slide 6: Winglet Design
P. Panagiotou, P. Kaparos, and K. Yakinthos found that a winglet with 50° cant angle is optimum at Re 1.2 million
This study uses 50° cant angle and varies sweep of winglet

## Slide 7: Winglet Design
Baseline: Schumann Tips
Case 1: No Winglet
Case 2: 30° Sweep
Case 3: 45° Sweep
Case 4: 60° Sweep
Case 2, 3, and 4:
  50 degree cant angle
  11.4 inches tall (equal to wing chord)
  0 toe and 0 twist angle

## Slide 8: Mesh Independence Study
Incrementally changed base size to ensure solution was mesh-independent
7 million cell mesh selected based on results

## Slide 9: Meshing Models
Mesh Base Size: .009m
Mesh Size: 7 million cells
Prism Layer Mesher
  Prism Layer Thickness: .007m
  Prism Layer Stretching: 1.2
Surface Remesher
Trimmer

## Slide 10: Physics Models
Steady
Constant Density
Segregated Flow
K-Omega Turbulence
Air conditions in Prescott, AZ to compare to wind tunnel data

## Slide 11: Wind Tunnel
A wind tunnel model was used to verify CL and CD data for the baseline model
Wind Tunnel vs. CFD
Data Here

## Slide 12: Results

## Slide 13: Conclusion
Schumann tips reduced induced drag cause by wingtip vortices. CL/CD increased at each AOA
Variable wingtip conclusion here

## Slide 14: Acknowledgements
Dr. Shigeo Hayashibara, ERAU
Joe Becar, Brigham Young University
Boeing AerosPACE Program