## Slide 1: Simulation of Material Characteristics and Laser Performance of Q-Switched Quantum Well Semiconductor Lasers
L. Chardee Allee
2014-2015 NASA Space Grant Symposium
18 April, 2015
Acknowledgements:
Dr. Rolf Binder (UofA)
Dr. Nai-Hang Kwong (UofA)
Dr. Paul Lundquist (Areté)

## Slide 2: Outline
Project Motivation
Introduction, quantum well lasers and Q-switching
Simulation framework
Matlab simulation
Conclusion

## Slide 3: Project Motivation
High power pulsed lasers have many applications (cutting and drilling, medical uses, measurement purposes such as ranging or LIDAR)
Q-switching typically employed in non-semiconductor lasers
Q-switching not well established for semiconductor lasers
Goal is to explore the possibility of Q-switching in semiconductor lasers, for example, a green gallium nitride laser

## Slide 4: What is a LASER?
Light Amplification by Stimulated Emission of Radiation
From: Saleh, Teich Fundamentals of Photonics (Wiley, 2007) p. 503
ΔE = Band gap energy, usually denoted Eg
No energy states exist between E1 and E2

## Slide 5: What is a LASER?
What is needed:
  Energy source (pump)
  Gain medium
  Resonator cavity (for example, mirrors)
Energy source (pump)
Resonator cavity
Gain Medium

## Slide 6: Quantum Well
Potential well with discrete energy values
Wave functions Probability density functions
From: Interaction Potentials, <http://www1017.vu.lt/legacy/pfk/funkc_dariniai/quant_mech/potentials.htm>

## Slide 7: Semiconductor Quantum Well Laser
Gain is within semiconductor material
From: Saleh, Teich Fundamentals of . . Photonics (Wiley, 2007) p. 729
Gain process within the active region

## Slide 8: Green Lasers
Frequency doubling is often employed to produce a green laser output
  Requires accurate alignment within the laser
  Not very robust
Current project looks to create a direct green laser
  Easier to build
  Very robust

## Slide 9: Q-Switching
Switching the quality factor, “Q” of the laser cavity such as changing reflectivity of mirrors
Bad cavity
  No lasing
  Build population inversion
Good cavity
  High power pulsed output

## Slide 10: Q-Switching
-
+
pump
rapid radiative and
non-radiative loss
Difficulty with Q-switching in
semiconductors: Requires fast
pumping and switching

## Slide 11: Semiconductor Model
N = Carrier density nh= Density of holes = Photon lifetime
S = Photon density ne = Density of electrons
Laser simulation model based on J. Mork, J. Mark, ‘Time-resolved spectroscopy of semiconductor laser devices: Experiments and modelling’, Proc. SPIE 2399, Physics and Simulation of Optoelectronic Devices III, 146 (June 19, 1995).

## Slide 12: Semiconductor Model
Quantity is switched from a large value (bad cavity) to a smaller value (good cavity).

## Slide 13: Simulation Results, Q-Switching
Note: Very preliminary results. Further parameter adjustment are needed.

## Slide 14: Simulation Results, Q-Switching
Bad Cavity
Good Cavity
Switch
Laser Pulse
Note: Very preliminary results. Further parameter adjustment are needed.

## Slide 15: Next Steps
Further adjust laser parameters to make model more realistic
Develop a program to numerically solve Schrodinger’s Equation
Create a better understanding for the behavior of the given quantum well
Further develop model to try and build this laser for testing

## Slide 16: Summary
Q-switched lasers are of practical importance
We are trying to explore Q-switching in semiconductor lasers
Utilizing theoretical simulation model for semiconductor laser dynamics
Explored parameter regimes for possible Q-switching

## Slide 17: Additional Slides

## Slide 18: Simulation Parameters

## Slide 19: Simulation Parameters

## Slide 20: Material Selection: III-Nitride System