## Slide 1: Effect of Flue Gas on Algae Growth
By Esteban Jimenez
Mentored by Dr. Kimberly Ogden
Department of Chemical and Environmental Engineering
Saturday, April 16th, 2016
University of Arizona

## Slide 2: Background - Algae
Beneficial and useful
  Food for both humans and animals
  Water treatment since species can filter impurities out
  My focus is on energy
How?
  More efficient to grow than trees or other plants
  Biomass can be turned into biofuel (ethanol and diesel)
  Does not increase CO2 emissions and reduces GHG

## Slide 3: Flue Gas
What is it?
  Exhaust gas from power plants after fuel combustion
  High CO2 concentration (most ~20%)
  UA Central Heating and Refrigeration Plant – 5%
Why is it important for us?
  CO2 sequestration from algae not efficient with air (~1%)
  Fuel made from this algae is greener than without flue gas
  Actually decreases CO2 emissions since it reduces amount released from factories
(Cuellar-Bermudez & Van Den Hende)

## Slide 4: Flue Gas - continued
Composition
  Mainly N2 and CO2
  Can also contain O2, H2O, NOx, SOx, CO, CxHy and other heavy metals
  Depends on composition of original fuel (coal vs. natural gas) as well as the reactor efficiency
Why we care
  Different algae have different tolerances to these compounds
  O2 and SOx can be toxic, must be regulated
(Van Den Hende)

## Slide 5: Objectives
Determine the biochemical effect that water saturated with flue gas had on algae growth
  Growth monitoring through Optical Density (OD)
  Analysis of metabolic products such as lipid content
Cultivating microalgae waste source by combining process to make it suitable – carbon dioxide fixation by microalgae using flue gas from UA power plant
  5% CO2

## Slide 6: Experiment Set up
Chlorella
Control
1 Hour
13 Hours
24 Hours
Notes: JM

## Slide 10: Conclusion and Moving Forward
Results are promising
  Flue gas did not have significant impact on growth, but did not decrease it either
  Time of exposure to flue gas does not appear to matter
  This means exposure time is irrelevant, and we can use CO2 to control the pH in outside setting
We want bigger
  To be efficient, this has to be able to work on industrial setting
  Much closer to what would be full-scale production of algae

## Slide 11: Power plant picture

## Slide 12: Power Plant

## Slide 13: Acknowledgements and Thanks
Margarita Acedo
Juan Sandoval
Dr. Kim Ogden
NASA Space Grant
University of Arizona
Algae

## Slide 14: Thank you!