## Slide 1: Laser Particle Image Velocimetry (PIV)
By: Michael Norville

## Slide 2: Laser PIV System
Particles
Googles
Router
Laser
Camera
Synchronizer
Test Specimen

## Slide 3: Procedure
Research on past PIV
  Types of systems
  Particles
Freestream Flow
Cylindrical Flow

## Slide 4: Particles
Particle Type | Size(μm) | Density (g/cm3) | Reflectivity | Company
Hollow Glass Spheres (HGS) | 18 - 81 | 0.23-1.15 | 1.52 | Potter LLC
Polyamide Seeding Particles (PSP) | 1 - 70 | 1.03 | 1.5 | Dantec
Fluoresecent Polymer Particles (FPP) | 1 - 100 | 1.5 | 1.68 | Dantec
Polysyrene Latex (PSL) | 0.4 - 0.6 | 1.05 | 1.55 | TSI
Metallic Coated HGS | 2 - 20 | 1.65 | 2.62 | TSI
Silicon Carbide | 1.1-1.9 | 3.2 | 2.65 | TSI
Titanium Dioxide | 3 - 5 | 4.2 | 2.6 | TSI

## Slide 5: Improving Lighting
Vary particle size
Vary particle reflectivity
Vary laser power
Adjust camera aperture
Adjust background light
Adjust time-step

## Slide 6: Improving Video Quality
Adjust time-step
Adjust water velocity
Adjust camera focus
Adjust camera distance from laser sheet
Adjust the distance from laser to the test object

## Slide 8: Cylinder Research

## Slide 9: Future Uses
Analyze various wing configurations
  Delta Wing
  Gurney Flaps
ERAU’s Experimental Aerodynamics class

## Slide 10: Special Thanks
Nick Valois
Dr. Lance Traub
Dr. Gary Yale

## Slide 11: References
"Tracer Particles and Seeding for PIV." University at Buffalo School of Engineering and Applied Sciences, n.d. Web. <http://www.eng.buffalo.edu/Courses/mae513/Lecture__Seeding_Particle_for_PIV.ppt>.
Melling, A. "Tracer Particles and Seeding for Particle Image Velocimetry." Measure. Science. Technology., n.d. Web. <http://iopscience.iop.org/article/10.1088/0957-0233/8/12/005/meta>.

## Slide 12: Questions?

## Slide 15: Equipment
200 mW red Laser (400-700 nm Class 3B)
Googles (certified to laser wavelength range)
Camera that provides 67 FPS at 780X580 pixels
Synchronizer
Particles (Hollow Glass Spheres: 18um-81um)
Water Tunnel (25Hz equivalent to 15 cm/s)
Computer
FlowEx Software
Gigabit Router

## Slide 16: Camera

## Slide 17: Software