## Slide 1: Computer Memory Testing System for Nano-Satellite
Matthew Demi Vis

## Slide 2: Overview
Purpose
Design Considerations
Design
  Hardware
  Software
Implementation

## Slide 3: Purpose
Now that Low Earth Orbit (LEO) is becoming easier to access, and nano-satellites are becoming more common, pressure for cheaper solutions to space-faring technology is on the rise.
Characterizing the risk of using Common Off The Shelf (COTS) data storage could make it feasible for use in low-cost systems.

## Slide 4: Design Considerations
Form factor
  For use in small, low-cost host system
Power Consumption
  Minimal impact on host system
Durability
  Endure rigors of launching to and being in LEO
Diverse COTS memory architectures
  Characterize risk in as many options as possible

## Slide 5: Design - Hardware
5 Common-of-the-shelf memory types
Microchip PIC24F microcontroller for low-power and high durability
Radiation shielded central controller to avoid erroneous errors.
Flash | Non-volatile | Susceptible
SRAM | Volatile | Susceptible
DRAM | Volatile | Susceptible
FRAM | Non-volatile | Theoretically resistant
MRAM | Non-volatile | Theoretically resistant

## Slide 6: Design - Software
Configurable data collection rate - power
  Sleep most time
  Different missions, different time periods
Communicate via UART to:
  request time for timestamping of data
  respond to requests for data
Error characterization
  Single-event upset
  Tie high/low bit
  Neighbor influence
  Latch up over time

## Slide 7: Implementation
Hardware
  Memory dispersed all around board
  CubeSat Kit bus for communication
  Central PIC will be shielded
Software
  Programmed in C
  MPLABX IDE
  XC16 compiler
  Cyclic Executive
IMAGE OF COMPLETE SYSTEM

## Slide 8: Review
Purpose
Design Considerations
Design
  Hardware
  Software
Implementation

## Slide 9: Acknowledgements
Arizona Space Grant Consortium
ERAU College of Engineering
Dr. Gary Yale
Dr. Brian Davis
Davis Gomez Herrera
Joskua Carrillo
Jason Lathbury