## Slide 1: OBC
Shawn Thompson
Demi Vis

## Slide 2: OBC Outline
Requirements
Concept of Operations
Subsystem Description
Development Environment/Tools
Theory of Operations
Bench-Test Development
Testing and Procedures

## Slide 3: OBC Requirements
Name | Description
CPU | A designated CPU is to be included on the OBC board.
Acceptable Performance | The central processing unit should be capable of meeting the processing demands of the payload boards.
Shutdown Command | CubeSats with batteries shall have the capability to receive a transmitter shutdown command, as per Federal Communications Commission (FCC) regulation.
Deployment Delay | Delay Spacecraft operation minimum 30 minutes after removal from launch vehicle.
Identification Transmission | At a known time-intervals, transmit identification of Spacecraft. (ARRL)

## Slide 4: Concept Of Operations
Main Objective: To capture GPS position data and store for later downlink
Bus voltage driven logic
is determined by a voltage divider on the EPS
State Name | Voltage Level | Description
Mode – 0 |  | No Satellite Function
Mode – 1 |  | Low-Power Mode
Mode – 2 |  | Enable Transceiver Receive
Mode – 3 |  | Enable Transmitter Transmit (Beaconing)
Mode – 4 |  | Enable GPS Lock Logic
State Name | Voltage Level | Description
Mode – 0 |  | No Satellite Function
Mode – 1 |  | Low-Power Mode
Mode – 2 |  | Enable Transceiver Receive
Mode – 3 |  | Enable Transmitter Transmit (Beaconing)
Mode – 4 |  | Enable GPS Lock Logic

## Slide 5: Subsystem Description - Hardware
Pluggable Processor Module by Pumpkin
  PIC24FJ - “eXtreme” Low-Power series
  Provides direct pin access for the motherboard
  Board Revision A
Flight Motherboard
  Provides programming/debugging interface
  Provides the interface to the CubeSat Kit Bus
  Integrated Real Time Calendar Clock (RTCC)
  Board Revision B

## Slide 6: Development Environment/Tools
All software development tools provided by Microchip
  Software Developed in ANSI C
  IDE: MPLABX v3.10
  Compiler: XC16 v1.25
  Programming/Debug Interface: ICD3
Header files and libraries provided by Microchip

## Slide 7: Theory of Operation
Interrupt Driven Design
  Six Interrupts to control software flow
  Power efficient and easy to debug
Interrupt Table
Interrupt Type | Interrupt Description
Analog Comparator | Eight volt trigger to turn off/on pertinent peripherals
Real Time Calendar Clock | Once-a-minute beacon that transmits satellite’s health and status data
GPIO – Energy Detect | Receive and parse a command from the Bell 202 Modem
GPIO – GPS Lock | GPS valid lock from pin on Novatel
Timer 1 | Manages GPS and COMMS subsystem communication and power
Timer 2 | GPS Lock Timeout – Two Minute Alarm

## Slide 8: Bench-Test Development
Hardware testing provided by Pumpkin Development Board – Revision D
Identical bus design and hardware functionality
Error checking
  Test points
  Replaceable hardware
  LED status indicators

## Slide 9: Testing and Procedures
First Cycle and Continuance:
  Description: Provide an accurate example of how the spacecraft functions on a typical basis with first flight procedure
  Procedure:
    Set power supply to a timer
    Monitor bus voltage
    Print status through UART for a period of time
Communications:
  Description: Determine the accuracy of receiving and transmitting with the implemented AX.25 protocol
  Procedure:
    Provide necessary voltages
    Transmit from ground station
    Monitor RSSI and valid packets received

## Slide 10: OBC Summary
All Requirements Met
Prototype software to be thoroughly tested by Early April.

## Slide 11: Backup Slides

## Slide 12: Mid-Level Connection Diagram