## Slide 1
EagleSat 2: Design Development Lauren Barthenheier Dr. Gary Yale, Embry-Riddle Aeronautical University Arizona Space Grant Consortium Symposium April 22, 2017

## Slide 2: Outline
Background
Initial Design
Design Change
Current Design
Conclusion

## Slide 3: Background
Goals:
Submit proposal to CSLI (CubeSat Launch Initiative) in November of 2017
Focus on commercially available bus systems (EPS, COMMS, ACS, OBC) to allow better payload development

## Slide 4: Initial Design Requirements
Fly three payloads
  Survey space debris and space dust
  Charged particle detector
    Pointing requirement: Must face away from earth
  Memory degradation experiment
Data Collection
  Space debris: 96 Mb per orbit
  Charged particle detector: 8 Mb per orbit
  Memory degradation experiment: 2.25 Mb per orbit

## Slide 5: Data Margins
Base: 17.6 W
Max Expected: 18.46 w
Max Possible: 19 W
Chart: 
| NASA Power Margin
Current Base Estimate | 17.59
Contingency | 0.8795
Margin | 0.5305
Base
Max
Expected
Max
Possible

## Slide 6: Power Margins
Chart: 
| NASA Data Margin
Current Base Estimate | 107.25
Contingency | 16.0875
Margin | 6.6625
Base: 107 Mb
Max Expected: 123 Mb
Max Possible: 130 Mb

## Slide 7: Decision Process
Denial
Anger
Bargaining
Depression
Acceptance
Pay
Want
Tech

## Slide 8: Cut Primary Payload
Stability requirements imposed on ADACS by Primary payload were too tight
Margins too tight for data and power
High cost

## Slide 9
Current Design

## Slide 10: Current Design Requirements
Fly two payloads
  Charged particle detector
    Pointing requirement: Must face away from earth
  Memory degradation experiment
Data Collection
  Charged particle detector: 40 Mb per orbit
  Memory degradation experiment: 2 Mb per orbit

## Slide 11: Expanding Payloads
Charged particle detector
CMOS imaging sensor
  Additional information from a second axis
Memory degradation
D-Type Flip Flops
  Determine if the circuit is corrupted due to space radiation
Radiation Hardened Chips
  Baseline for data

## Slide 12: Power Margins
Base: 15 W
Max Expected: 16 W
Max Possible: 19 W
Chart: 
| NASA Power Margin
Current Base Estimate | 14.82
Contingency | 1.482
Margin | 2.698

## Slide 13: Data Margins
Chart: 
| NASA Data Margin
Current Base Estimate | 11.25
Contingency | 1.6875
Margin | 12.0625
Base: 11.25 Mb
Max Expected: 12.9 Mb
Max Possible: 25 Mb

## Slide 14: Solar Panel Design
Three 3U solar panels fulfill power requirements
One solar panel needs to be deployed so all three can see the sun at the same time

## Slide 15: Internal Configuration
Internal volume: 2,320 cm3
Occupied volume: 1,200 cm3
Volume margin: 48.3%

## Slide 16: Conclusion
Cut primary payload
  Reduced costs and data requirements
Expanded charged particle detector and memory degradation experiment
Deployable solar panel to meet power requirements

## Slide 17: Acknowledgements
Dr. Gary Yale, Embry-Riddle Aeronautical University
TeamXC, NASA Jet Propulsion Laboratory
Travis Imken, NASA Jest Propulsion Laboratory

## Slide 18
Thank You