## Slide 1: ESFT : Propulsion Team Solid Propellant Propulsion
Rebecca Tobin
tobinr@erau.edu
Mentor: Dr. Brenda Haven

## Slide 2: Outline
Propellant
Characterization
Previous Geometry Design
Current Geometry Design
Casting Methodology
Future Objectives

## Slide 3: Current Propulsion Team Mission
Design an optimized grain geometry to match a desired thrust profile
Design a casting method
Static Fire and compare theoretical and experimental data

## Slide 4: Solid Propellant
Current Formula:
72% Ammonium Perchlorate
  Allows a castable form of propellant, which allows the manufacturing of desired geometries
7% Aluminum
  High Energy Fuel
2% Oxamide
  Burn Rate Reduction
14.08% HTPB
  Hydroxyl-terminated Polybutadiene- Elastomer Binder
2.12% E-744
  Curing Agent
1.8% IDP
  Inosine Diphosphate

## Slide 5: Characterization
Three static firings with three different nozzle throat areas for data acquisition
Data analysis in Mathematica
St. Robert’s Law:
  Burn Rate: 0.7825
  Burn Rate Coefficient: 0.0543397
  Chamber Pressure:
  Pressure Exponent: 0.416039

## Slide 6: Previous Grain Geometry
Multiple grains, three different nozzle throat areas tested
Bates Grain Geometry (tubular)

## Slide 7: Optimized Grain Geometry
Desired thrust profile wanted an initial spike followed by a progressive burn
Developed a MatLab code to run through a star grain geometry with variable parameters for optimization

## Slide 8: Combined Geometries
Desired thrust profile required a larger initial spike
Combined a bates grain and an optimized star grain

## Slide 9: Casting Methodology
Casting Cup
Removable Bore
Removable Cap
Removable Base

## Slide 10: Propulsion Testing
Motors placed in a liner
Liner placed in casing
Forward and aft closures are sealed with O-rings
Fully assembled motor is mounted and static fired

## Slide 11: Future Objectives
Larger propulsion system scaling
Optimizing nozzle geometry
6in diameter flight motor

## Slide 12: Acknowledgements
Dr. Gary Yale – ERAU Space Grant Coordinator
Dr. Brenda Haven – Project Mentor
Dr. Michael Fabian – Guidance
Undergraduate Research Institute