## Slide 1: Anammox
Anaerobic Ammonium Oxidation (Anammox) for Nitrogen Removal
Abdullah Matalgah
Mentor: Dr. Reyes Sierra
Dept. Chemical and Environmental Engineering
April, 14, 2018

## Slide 2: Our Objective is to Remove Ammonium

## Slide 3
Ammonium Issues:
Ammonium-NH4+ in water causes public health threats and fish toxicity
NH4+ is present in municipal wastewater at high concentration
The conventional method of NH4+ removal is energy intensive with high C-footprint

## Slide 4
Solution:
The Anammox process removes NH4+ more economically with less C-footprint
Anammox: NH4+ + NO2- → N2 + 2H2O
The performance of the Anammox process will be investigated in an expanded granular sludge bed (EGSB) bioreactor

## Slide 5
Mechanisms:
Double Time:
  Anammox: 9-10 days
  E-Coli: 20 minutes

## Slide 6: EGSB Bioreactor

## Slide 7
EGSB: Expanded Granular Sludge Bed
The reactor was continuously fed with synthetic wastewater
The performance was monitored by measuring the Nutrient-N (NH4+ & NO2-) in influent and effluent samples using ion chromatography
Also, the volume of N2 gas produced was measured over time

## Slide 8
Twin Nursing Reactors:
Temp: 30°C
HRT: 0.21 day
Influent:
  Ammonium: 502 mg/L
  Nitrite: 1440 mg/L
R3
R4
N2 bubble

## Slide 9
Average Removal (g/Lreactor -day) (IC) | 
NH4+ | 1.59 ± 0.30
NO2- | 4.78 ± 0.71
Chart: Influent R3
| 43129 | 43131 | 43133 | 43136 | 43138 | 43140 | 43143 | 43145 | 43147 | 43150
Ammonium | 580.2341 | 587.1323 | 481.5328 | 562.6421 | 456.3856 | 402.2506 | 440.9497 | 471.6506 | 431.9415 | 670.0585
Nitrite | 1651.3029 | 1622.1096 | 1367.4775 | 1536.1354 | 1301.1147 | 1162.7558 | 1323.2005 | 1301.8254 | 1240.2799 | 1791.136
Chart: Effluent R3
| 43129 | 43131 | 43133 | 43136 | 43138 | 43140 | 43143 | 43145 | 43147 | 43150
Ammonium | 62.0395 | 57.036 | 35.152 | 38.0301 | 32.9165 | 41.6754 | 29.173 | 40.6091 | 35.7067 | 12.1638
Nitrite | 36.3263 | 29.5742 | 6.2248 | 14.53 | 15.2803 | 55.0953 | 5.3693 | 11.845 | 7.6463 | 0
N2 gas production (g/Lreactor -day) (Gas Meter) | 
Expected | 2.52
Measured | 1.54

## Slide 10
Average Removal (g/Lreactor -day) (IC) | 
NH4+ | 1.56 ± 0.22
NO2- | 4.92 ± 0.74
Chart: Influent R4
| 43129 | 43131 | 43133 | 43136 | 43138 | 43140 | 43143 | 43145 | 43147 | 43150
Ammonium | 561.4649 | 611.8286 | 441.8264 | 522.964 | 451.8346 | 437.211 | 434.9498 | 443.2225 | 454.0073 | 595.5747
Nitrite | 1847.6536 | 1715.4281 | 1287.3736 | 1502.309 | 1316.9617 | 1291.1642 | 1288.137 | 1283.3197 | 1307.8536 | 1654.0669
Chart: Effluent R4
| 43129 | 43131 | 43133 | 43136 | 43138 | 43140 | 43143 | 43145 | 43147 | 43150
Ammonium | 41.301 | 28.9949 | 24.7389 | 27.6311 | 31.563 | 33.0835 | 32.4468 | 25.2082 | 49.5141
Nitrite | 17.294 | 8.5413 | 5.3429 | 5.3298 | 33.9703 | 10.4366 | 8.0543 | 5.7378 | 11.1474
N2 gas production (g/Lreactor -day) (Gas Meter) | 
Expected | 2.47
Measured | 2.46

## Slide 11: Anammox Activity Bioassay

## Slide 12: Batch Activity Test
To determine the max. specific anammox activity of the biomass, i.e., amount of N2 gas per gram of dry biomass and per day.
The experiment is performed in a 160ml serum flask
  100ml synthetic wastewater medium
  60ml Helium gas
  0.5g biomass
Using Gas Chromatography, the N2 content in gas samples is evaluated six times, once per hour.

## Slide 13: Anammox Activity Bioassay
Basal medium
Biomass
He
Bottle Vol. = 160 ml
Liquid Vol. = 100 ml (Total)
Liquid & headspace flushing with He (6 min each)
Addition of substrate
NH4+ = 5.4 mM
NO2- = 7.1mM
Biomass taken from a granular enrichment culture (Brocadia spp.)
He

## Slide 14
Chart: Nitrogen Gas Production
| 0.10172453703853535 | 0.15403935185167938 | 0.21731481481401715 | 0.28978009259299142 | 0.36792824073927477 | 0.96843749999970896 | 1.1075810185211594
R3 | 0.041072 | 0.09783 | 0.14774 | 0.22901 | 0.28898 | 1.06 | 1.2425
R4 | 0.056464 | 0.095427 | 0.15372 | 0.23437 | 0.31652 | 1.016 | 1.2293

## Slide 15
Chart: Max. Specific Anammox Activity of the Reactor Biomass
R4 | 0.99126
R3 | 0.93671

## Slide 16: Conclusions
The continuous Anammox bioreactors provided high NH4+ and NO2- removal efficiency (93% on average).
Based on the batch bioassays, the max. specific activity of the biomass was 1 g N/(gram dry biomass x day).
Due to the advantages of the Anammox Process, Pima County Water Reclamation Department is interested in implementing this process.

## Slide 17: Acknowledgements
I would like to thank Dr. Reyes Sierra for introducing me to the water treatment field which made me more determinant of my future careers.
Special Thanks to Dr. Guangbin Li, Nivrutti Lakhey, Derek Swartzendruber, and Hezhou Ding for teaching and assisting me in the lab work.
Also, Thanks to NASA Space Grant for its support during this internship experience.

## Slide 19
Appendices

## Slide 20
Influent: 1 NH4+ +1.32 NO2- +0.066 HCO3- + 0.13 H+
Effluents: 1.02 N2 +0.026 NO3- +2.03 H2O +CH2O0.5N0.15
Mechanisms:
https://en.wikipedia.org/wiki/Anammox

## Slide 21
https://www.ugent.be/bw/biosysteemtechniek/en/research/biosystems-control/completed_research_projects/research-castrobarros.htm

## Slide 22
Serum flask
Anammox Bacteria
Medium
Helium gas
Sealing Cap