## Slide 1: EagleSat 2 – Electrical Power Subsystem Development
Presented by: Chloe McClellan – Electrical Power Lead
In cooperation with: Dr. Gary Yale, Hilliard Paige, Jason Hamburger, Steven Buck, David Stockhouse, and Lauren Barthenheier
27th Arizona Space Grant Symposium
Tempe, Arizona
April 14nd 2018

## Slide 2: Outline
Background Information
  Mission Considerations
Power Budget
  Subsystem Power Consumptions
  Power Budget Visual
Hardware
  Solar Panels
  EPS Board
  Battery
Conclusions
  Testing
  Summary

## Slide 3: Background Information

## Slide 4: Mission Considerations
Objective – to provide electrical power to bus and payload subsystems
Design Factors – spacecraft size, solar cell surface area, robustness of hardware, orbit path

## Slide 5: Power Budget

## Slide 6: Subsystem Power Consumptions
SUBSYSTEM | PEAK POWER CONSUMPTION (W) | TYPICAL POWER CONSUMPTION (W)
Communications | 2.7 | 0.1
On Board Computer | 0.9 | 0.5
Cosmic Ray Payload | 1.8 | 0.4
Memory Degradation Payload | 0.2 | 0.2
Attitude Determination and Control | 1.2 | 0.7
Structure | 0 | 0
Electrical Power | 0.3 | 0.3
Total | 7.1 | 2.2
Notes: Double check values with team leads

## Slide 7: Power Budget
Notes: Worst case scenario
Start in eclipse

## Slide 8: Hardware

## Slide 9: Solar Panels
3U solar panels by Clydespace
7 Watt generation (BOL)
Configuration: Two custom, two original
  Custom panels will have once cell removed
  Alternating custom and original on long faces

## Slide 10: EPS Board
Clydespace 3rd Gen FlexU
Designed to support high power spacecraft
< 90% effieiency
Higher number of battery charge
regulators and other safety features

## Slide 11: Battery
Clydespace 40 Whr Battery
Capacity great enough to continue operations while in eclipse
Lithium Polymer battery in 2s4p configuration
Complies with NASA EP-Wi-032
Multiple protection features

## Slide 12: Conclusions

## Slide 13: Testing
High Altitude Balloon
  Ensure payloads are functional
Clyde-Space Validation
  Ensure battery is safe for manned missions

## Slide 14: Summary
Battery reaches full capacity within 16 orbits under worst-case scenario conditions
Depth of discharge is less than 10% after reaching full capacity
Power budget is robust enough to accommodate greater than typical consumption without damaging components

## Slide 15: Acknowledgements
Dr. Gary Yale, Embry-Riddle Aeronautical University
Travis Imken, Jet Propulsion Laboratory
Dr. Julio Benavides, Embry-Riddle Aeronautical University