## Slide 1
Deborah Jackson
Embry-Riddle Aeronautical University Aerospace Engineering, Sophomore
AZ/NASA Space Grant Symposium
April 14, 2018
EagleSat-1 Project: Mission Synopsis

## Slide 2: Presentation Overview
Mission Overview
Satellite Structure
Satellite Testing
Integration and Launch
Satellite Communications
Failure Analysis
Next Steps
Future of EagleSat-1

## Slide 3: Mission Overview
Primary Objective: Educational
Secondary Objectives:
  Primary: Orbital decay
  Secondary: Supercapacitors
Notes: Operational goals:
Determine position periodically to approx decay
Store data for transmission
Downlink at request
Beacon identity and telemetry

## Slide 4: Satellite Structure

## Slide 5: Satellite Structure: GPS
Novatel OEM615

## Slide 6: Satellite Structure: Comms
Taoglas Antenna Ceramic GPS Patch for RF
Wood and Douglas Radio Module

## Slide 7: Satellite Structure: Power
Eaton HV1030-2R7106-R 10F (3V) Supercapacitors
Provides 4F (15V)

## Slide 8: Satellite Structure

## Slide 9: Satellite Testing
Day in the Life Test: software verification
Random Vibration: launch vehicle
Shock: launch vehicle
Thermal Bakeout: outgassing

## Slide 10: Integration and Launch
NASA (2017)

## Slide 11: Communications
Notes: 437.645 MHz
monopole, steel, 17.8 cm long, 25 degrees from top of structure
Yagi, 23 elements

## Slide 12: Ground Station
TNC
Rotator and Azimuth
Power Supply
Kenwood Radio
Pre-Amp
Ham Radio Deluxe
Notes: Azimuth: 450 deg
Elevation: 180 deg

## Slide 13: Data Flow

## Slide 14: Failure Analysis: Silent Treatment
Antenna not deployed
Discharging before transmitting
  Shorting near solar cells
  GPS consuming
Damaged solar cells
Damaged critical components
United Launch Alliance (2018)

## Slide 15: Next Steps
Surrounding frequencies
Old frequency
Eclipsed and non-eclipsed passes
Visual confirmation
4.5 meter dish
Rfhamdesign.com

## Slide 16: Future of EagleSat-1
Estimated Life span: 1-2 years
Orbit Life span: 7-9 years
GPS data will analyze models for small satellites
Notes: Observe, propagate, observe, present discrepancies

## Slide 17: Acknowledgements

## Slide 18: Questions? Deborah Jackson jacksd40@my.erau.edu “Success is not final, failure is not fatal: it is the courage to continue that counts.” Winston Churchill

## Slide 19: Citations
NASA (2017), JPSS Launch 3a [Online Image]. Retrieved March 23, 2018 from https://www.nasa.gov/press-release/nasa-launches-noaa-weather-satellite-aboard-united-launch-alliance-rocket-to-improve.
United Launch Alliance (2017), Delta II JPSS-1 Mission Profile [Screenshot]. Retrieved March 23, 2018 from https://www.youtube.com/watch?v=tLkbdYZyf1c
User picture 4.5 Meter Dish [Online Image]. Retrieved on March 23, 2018 from http://www.rfhamdesign.com/products/parabolicdishkit/45meterdishkit/index.php.