## Slide 1: Cadmium Removal from Water with a Corn Biosorbent
By Melissa Jacquez
Environmental Engineering department Northern Arizona University
Mentor Dr. Fethiye Ozis

## Slide 2: Importance of clean water
Mine spills effecting rural commutes
  Chenzhou mine spill (China)
  Tar Creek superfund site
  Kings mine spill
    Cd 36.1 μg/L to 138 μg/L
  Cadmium health effects
  Short term exposure:
    nausea, vomiting, diarrhea, muscle cramps, sensory disturbances, liver injury and renal failure
  Long term exposure:
    kidney, liver, bone and blood damage

## Slide 3: Bio-sorbents?
Biosorbents- tiny particles of any biological component that remove metals or nonmetals from a solution .
United States produces 120 million tons of biomass residue per year
Corn is a possible economically way to remove heavy metals from water.
Question: Do corn cobs work as a viable biosorbent to remove Cadmium from contaminated waters?

## Slide 4: Data collection

## Slide 9: 10 ug/l 25 ug/l 80 ug/l

## Slide 12: Analysis
Calibrated data points |  |  | 
 | Test 1 | Test 2 | Test 3
Ci (ug/L) | Cf (ug/L) | Cf (ug/L) | Cf (ug/L)
10 | 11.08 | 7.13 | 14.41
25 | 14.67 | 33.41 | 14.41
80 | 42.95 | 28.84 | 45.52
Chart: Calbrated
| 7.1260500000000002 | 14.671560000000003 | 14.414909999999999 | 42.954389999999997 | 45.520890000000001
 | 0.86218 | 3.0985 | 3.1755 | 11.1137 | 10.3437
data points | 0.86218 | 3.0985 | 3.1755 | 11.1137 | 10.3437

## Slide 13: Conclusion
Initial concentration (ug/L) | Removal/Absorption Efficiency
10 | 9.0 %
25 | 41.8 %
80 | 51.1 %
For higher concentrations corn is a viable biosorbent
Lower concentration did not see large sorption rates.
Is a viable bio sorbent for Cd but further research could be done on different parts of the corn and other heavy metals.

## Slide 14: Special thanks to Dr. Ozis Nasa Space Grant Any Questions?