## Slide 1: Flat Earth Society
Jose Inzunza Juan Pablo Garcia
Jennifer Bartelme Marina Sliwo

## Slide 2: Objectives
Minimum
  Weight
  Imaging
  Sensors
System Block Diagram
Runcam
Desired
  Biology
  Telemetry
  GPS

## Slide 3: System Block Diagram

## Slide 4: System Components
Temperature
Sensor Internal
And External
Accelerometer
UV Sensor
Pressure

## Slide 5: Payload Assembly

## Slide 6: Etching the Circuit Board

## Slide 7: Constructing the payload

## Slide 8: Global Navigational Satellite System

## Slide 9: Positioning System
Can make use of all major satellite constellations
Accuracy improvement of 4x over GPS
Max 22 satellite fix
UBLOX NEO 6M-GPS

## Slide 10: Positioning System Output
Data output in NMEA sentence
Sentence uses header $xxxxx to define information type
Sentence then parsed for necessary information
Position, Altitude data stored every 2 seconds

## Slide 11: MODEM

## Slide 12: The RockBLOCK Modem
•It relies on the IRIDIUM constellation (66 satellites)
•Cost: 250$
•1¢ per byte

## Slide 13: On the Ground / In vehicle
Temperature, pressure, battery voltage, current timestamp, and GPS data were received and interpreted.

## Slide 14: Inside the payload
50 bytes of data every minute.
Payload status at 30 and 60 seconds.

## Slide 15: CAMERA

## Slide 16: Fall 2018 360 Fly
360 HD Footage
Dustproof, shockproof, and water resistant
2+ hours of recording time

## Slide 17: Spring 2019 RunCam 2

## Slide 19: BACTERIA SURVIVAL

## Slide 20
Compared to control conditions on the ground.
Deinococcus
Escherichia coli
Externally in Dome
Internal of Payload
Internal conditions :
Internal temperature range -> 35 F to 90 F
Pressure range -> 0.94 atm to 0.02 atm
Dome conditions:
Temperature range -> 10.4 F to 116 F
Pressure range -> 0.95 atm to 0.02 atm
UV Index range -> 1 to 6

## Slide 21: TESTS AND CHALLENGES :
WHAT COMMON MEDIA IS BEST TO DECREASE THE VARIABLES?
  Both bacterias were tested on same temperature of 37 celcius over two nights to find common media.
  Liquid TS (Typticase Soy Agar).
WOULD DEINOCOCCUS SURVIVE LOW TO ZERO OXYGEN?

## Slide 22
Bacteria/Media Ratios and Results Table:

## Slide 23: Biological Testing Methods:
Spectrophotometer:
Determine the optical density of a bacteria culture.
Streak plate to isolate colonies.

## Slide 24: Dilution and Plate Count:

## Slide 25: Results:
Inside: Both bacterias survived with lower growth comparing to controlled ones.
Outside: Both bacterias died.
Controlled: Both bacterias grew in higher rated comparing to the inside ones.

## Slide 27: Future Improvements:
Do replicas of each vial.
Design the payload so that the bacteria in the dome experiences actual atmospheric temperatures.
Include a GEIGER Counter for radiation.

## Slide 33: Data

## Slide 34
Elevation Spring 2019
Traveled up to 96,000 ft at ~17.5 ft/s
Traveled down to 0 ft at ~60 ft/s
Launch ~1500s, balloon burst ~7000s, landing ~8700s. Total flight time 120 min.

## Slide 35: Temperature vs. Elevation

## Slide 36: Internal Temperature
Fall 2018
Spring 2019
Notes: Data analysis covers a full collection time from pre-launch to recovery of 11,867s. Launch time began at 1380s. The payload traveled at approximately 19.5ft/s until the balloon burst at 106,600 feet at 6,780s and landed at 9,000s. Min -15F (-26C)

## Slide 37: External Temperature
Fall 2018
Spring 2019

## Slide 38: Pressure
Fall 2018
Spring 2019
Notes: Begins at a maximum of 0.95atm at a launch altitude of 1,200ft and decreases to a minimum of 0.02atm at the time of balloon burst at an altitude of 106,600ft observing a similar reverse pattern as the payload descends again reaching 0.91atm at a landing altitude of 1,490ft.

## Slide 39: Acceleration X-direction
Fall 2018
Spring 2019

## Slide 40: Acceleration Y-direction
Fall 2018
Spring 2019

## Slide 41: UV Index
Fall 2018
Spring 2019
Notes: Many factors account for changes in UV index such as time of day, cloud cover, ozone levels, etc. The data depicts a general trend in which the UV index increases with elevation and time of day

## Slide 42
THANK YOU
Dr. Tim Frank Rick Sparber
Dr. Lucrecia Alvarez Rhonda Lee
Arizona Space Grant NASA ANSR

## Slide 43
Questions?