## Slide 1: Embry-Riddle ASCEND
Thomas Montano

## Slide 2: Project Goals
Demonstrate that Software defined radios can replace typical hardware-based systems
Demonstrate that SDR's will offer a higher performance, and lower developmental cost

## Slide 3: Software Defined Radio Transceiver
LimeSDR Mini
Allows flexibility and development
Programmed with GNU Radio

## Slide 4: Onboard Computer
ARM Cortex-A9 Quad Core Processor and ARM Cortex-M3
76 GPIO Pins
Main digital signal processor

## Slide 5: Onboard Antenna Characteristics
Two monopoles (SISO)
2 dBi total gain
Horizontal polarization

## Slide 6: Ground Station Antenna Characteristics
Single Wavelength folded Dipole
24 dBi total gain
Horizontal polarization

## Slide 7: Monopole Antenna Resonance

## Slide 8: Monopole Antenna Gain

## Slide 9: Link Budget
Operational Parameters
  2 Watts downlink power
  2 dBi payload antenna
  24 dBi ground station antenna
  500 kHz total bandwidth
  2-GFSK Modulation
Theoretical Signal Characteristics
  93.63 SNR from ground to payload
  65.56 (Energy per bit to Noise Ratio)
Theoretical Received power stays above noise floor

## Slide 10: Signal Strength Theory
Published Friis Transmission Equation:
Solving for received power:
Used to obtain SNR

## Slide 11: Data Rate Theory
Shannon Hartley Theorem:
Theoretical data rates for an assumed SNR
Given system parameters, a data rate of
~2.5 Mbps should be expected
Actual data rate is closer to 2 Mbps

## Slide 12: Receiver Flowchart

## Slide 13: Transmitter Flowchart

## Slide 14: Experimental Results
Signal confirmation for 25 miles
Received power matches theoretical
Performance was equal to hardware system

## Slide 15: Questions?