## Slide 1
Low Frequency Unsteadiness in Laminar Separation Bubbles
Alek Cotnoir
NASA Space Grant Undergraduate Research Symposium
April 17th, 2021
Mentor: Dr. Jesse Little
Department of Aerospace and Mechanical Engineering
Partially Funded by NSF

## Slide 2: Laminar Separation Bubble (LSB)
Form in wall bounded flows when subjected to a strong adverse pressure gradient
Area of slow moving/circulating air
Modifies effective shape of airfoil
Impacts aerodynamic performance
Winslow, J., Otsuka, H. ,Govindarajan, B., Chopra, I., “Basic Understanding of Airfoil Characteristics at Low Reynolds Numbers,” Journal of Aircraft, Vol. 55, No. 3. May-June 2018

## Slide 3: Low Frequency Behavior in the LSB
Expansion and contraction of LSB called ‘breathing’
Observed in subsonic to supersonic regimes
Breathing frequency increases as bubble size decreases
Detrimental to aircraft performance
  Loss of lift
  Component fatigue
  Propulsion system complications
Weiss, J., Little, J., Threadgill, J., “Low-Frequency Unsteadiness in Pressure-Induced Separation Bubbles,” AIAA Sci-Tech Forum. January 2021
Strouhal Number =>

## Slide 4: Experimental Setup
Aluminum honeycomb plate
  78 in. x 47.75 in. x 0.5 in. (1.98 m x 1.22 m x 13mm)
  1mm solid aluminum skin
  Flatness: +/-0.665 mm/m (+/-0.008 in./Ft.)
Leading edge:
  1:20 superellipse (Lin et al. 1992)
Adjustable trailing edge flap
Elevated to 8.25 in. above the tunnel floor
Displacement Body:
  8 in. chord x 46 in. span
Flow
Leading Edge
Adjustable Flap
Flat Plate
Wing
Sting
CTA Probe
Plasma Actuator

## Slide 5: Equipment
Constant Temperature Anemometry (CTA) Probe
Small wire between two prongs
Current run through wire
Airflow changes temperature (and thus resistance) of wire
Resistance measured and airflow speed known
Good for frequency measurements
Alternating Current Dielectric Barrier Discharge (AC-DBD) Actuator
Active flow control
Provide flow with disturbances of known frequency and amplitude
Moreau, E., “Airflow Control By Non-Thermal Plasma Actuators,” J. Phys. D: Appl. Phys., 40 605, 2007

## Slide 6: PSD at Shear Layer for Different Forcing Amplitudes
Sampled at 2500 Hz
Forced at 245 Hz
Shedding frequency at 245 Hz
Very little frequency content in freestream
PSD (
Frequency (Hz)
Measurement Location

## Slide 7: Pre-Multiplied PSD at Shear Layer for Different Forcing Amplitudes
6 Hz ‘breathing’ with no forcing
30 Hz ‘breathing’ with 5 kVpp forcing
Transition to turbulence likely with 8 and 12 kVpp forcing
Smaller bubble size =>measurement is further downstream relative to bubble
Frequency (Hz)
Frequency (Hz)
f*PSD (
f*PSD (

## Slide 8: Effect of Forcing on Bubble Size
Higher forcing amplitude reduces bubble size

## Slide 9: Conclusion
‘Breathing’ behaves as expected
  Forcing => smaller bubble size
  Smaller bubble size => higher breathing frequency
  Forcing => higher breathing frequency
Next Steps
Optimize forcing
  Decrease actuator height
  Decrease distance between actuator and bubble
  Decrease required forcing amplitude
  Eliminate turbulent behavior

## Slide 10: Acknowledgements
Dr. Jesse Little
Dr. James Threadgill
David Borgmann, PhD Student
The Aerospace and Mechanical Engineering Department
The Arizona Space Grant Team
National Science Foundation

## Slide 11
Thank You