## Slide 1: SUBORBITAL CREWLESS AERIAL VEHICLES FOR EARTH SURVEILLANCE & MARS EXPLORATION
MADDIE SCHIFFLER & REED SPURLING
MENTOR: SERGEY SHKARAYEV
COLLABORATOR: ADRIEN BOUSKELA
SPACE GRANT SYMPOSIUM
APRIL 17, 2021

## Slide 2: PROJECT GOAL: SAILPLANES FOR MARS
Sailplanes, imitating albatrosses, can theoretically fly for days without landing
  Dynamic soaring
High-altitude flight on Earth
  Mapping
  Climatology
  Telecommunications
Low-altitude and mid-altitude flight on Mars
  Imaging interesting geology in rugged highlands
  Canyon exploration
  Close-up investigations of crater interiors
Higher pixel-scale image resolution than orbiters
More mobility than landers or rovers
Image credit: Parisa Footohi
Notes: Backup slides:
ConOps diagram
Dynamic soaring

## Slide 3: WHAT WE’VE BEEN DOING THIS YEAR
To develop, assemble, and test a weather balloon-based system to support experimental flights of a prototype sailplane at altitudes up to 100,000 feet above Earth’s surface, where the atmosphere is similar to Mars’ atmosphere.
Thus far, we have launched this system twice, once without our sailplane—to verify the accuracy of our calculations and the proper functioning of electronics and telemetry systems—and once with the sailplane to test the preparedness of our ground station and balloon release mechanism

## Slide 4: FIRST TEST FLIGHT (NO SAILPLANE)
Goals:
  Balloon helium lift calculation and launch procedure verification
  Wind measurement system tests
  Preliminary ground system tests

## Slide 5: INFLATING + RELEASING
Discovered that we need a system to make filling and releasing the balloon easier
Helium calculations were accurate, bringing the payload up to altitude at a rate of 5 m/s

## Slide 6: WIND MEASUREMENTS
  In order to study the wind shears and gusts that enable dynamic soaring, we need accurate measurements
  We 3D printed a multi-directional pressure sensor for this flight test
  Ended up with a lot of inaccuracies in the data and concluded that a new system needs to be developed

## Slide 7: GROUND SYSTEM TESTS
The ground system code worked
  Live telemetry from the balloon payload
The hardware took a long time to set up
The antennas did not automatically point in the right direction
Next steps
Redesign antenna pointing hardware
Improve ease of assembly and use
Improve code
  Readability
  Autonomy

## Slide 8: SECOND FLIGHT TEST (TETHERED)
Testing goals:
  Ground system operation
  Telemetry connection/ground station capabilities
  Balloon housing aptitude
  Release mechanism capability & optimal release pitch angle

## Slide 9: GROUND STATION
Video Display
  First-person view (FPV) available
Sailplane can be directly controlled from one or many laptops
Still too complicated
  Setup should ideally take just a few minutes

## Slide 10: IMPROVED ANTENNA SYSTEM
Two antennas
  Video receiver
  Telemetry receiver and controller
3D-printed enclosure
Off-the-shelf components
  Camera tripods
  Raspberry Pi computers
  Compass/GPS modules
  Wiring
Inexpensive!
Notes: maybe add in more CAD models

## Slide 11: BALLOON HOUSING
Made inflating and releasing the balloon easier

## Slide 12: RELEASE MECHANISM
Necessary for safe and reliable separation of the sailplane from the balloon
Many iterations made before landing on this design, positioned at the center of gravity and fits around the plane shape
Notes: add picture

## Slide 13: OPTIMAL PITCH ANGLE
  Pitch angle is the angle at which the plane is oriented: pitch up - nose up, pitch down - nose down
  Pitched down works best with release mechanism
  Flight mode recovers best with this pitch angle of approximately -30°

## Slide 14: WHAT MADDIE WILL BE WORKING ON
Continue work on the release system as necessary
Multi-hole probe pressure sensor for wind measurements + testing
Based on research done by students at Oklahoma State University, Stillwater, OK

## Slide 15: WHAT REED WILL BE WORKING ON
Further improved antenna pointing system design
  Modular design to enable easy component swaps
  Press-fit assembly with fewer bolts
  Better electrical connections
  Fully automated

## Slide 16: THANK YOU! Sailplanes and dynamic soaring methods expand the possibilities for planetary exploration! We are continuing to develop this technology and plan to demonstrate its feasibility in upcoming high-altitude flight tests.
Professor Sergey Shkarayev
Adrien Bouskela
Arizona Space Grant Consortium
Aerospace and Mechanical Engineering Department