## Slide 1: Influence of woodland encroachment on vegetation, soils, hydrology, and erosion on sagebrush rangelands
By: Trisha Jean Lane
Mentor: Jason Williams, Research Hydrologist, USDA-ARS Southwest Watershed Research Center
Funding Entities – USDA-ARS Southwest Watershed Research Center; USDI-Bureau of Land Management; University of Arizona – Arizona Space Grant Consortium
April 22, 2023
Arizona Space Grant Consortium Symposium

## Slide 2: Woodland Encroachment into Sagebrush Steppe
Figure 1. Sagebrush Rangeland

## Slide 3: Woodland Encroachment into Sagebrush Steppe
Reduced vegetation and ground cover
  increased runoff, erosion, & soil loss.
Sustained reduction in delivery of ecosystem services.
Figure 2. Woodland with downslope channel erosion
Figure 3. Woodland with extensive bare area
Figure 4. Woodland with rills
Figure 5. Sagebrush Steppe
Figure 6. Woodland with dead sagebrush

## Slide 4: Problem
Land managers at Grand Staircase Escalante National Monument and elsewhere need an improved understanding of the impacts of woodland encroachment on vegetation, hydrology, and erosion processes to aid management decisions and guide conservation planning.
Field studies to assess woodland encroachment effects are commonly resource-demanding and logistically challenging.
The Rangeland Hydrology Erosion Model (RHEM) has recently been evaluated for predicting the effects of woodland encroachment on hydrology and erosion and provides a useful tool for assessing impacts and guiding management.

## Slide 5: Study Area
Grand Staircase Escalante National Monument
Site info:
Latitude: 37.27°; Longitude: -112.37°
Elevation: 1840 m
Annual Precipitation: 400 mm; Annual Air Temperature 10°C
Vegetation:
  Sagebrush steppe
  Pinyon-Juniper Woodland (Woodland-Encroached Sagebrush Steppe)
Figure 7. Woodland study area
Figure 8. Sagebrush study area

## Slide 6: Research Purpose
GOAL:
Determine hillslope-scale ecohydrologic and erosion impacts of woodland encroachment on sagebrush rangelands at Grand Staircase Escalante National Monument.
Figure 9. Source: https://apps.tucson.ars.ag.gov/rhem/

## Slide 7: Research Purpose
Specific Objectives:
Using commonly applied field methods, quantify woodland encroachment impacts on hillslope-scale vegetation structure and patch-scale vegetation and ground cover.
Quantify the impacts of woodland encroachment on hillslope-scale runoff and soil loss using patch-scale modeling with the RHEM web tool.
Figure 9. Source: https://apps.tucson.ars.ag.gov/rhem/

## Slide 8: Methods: Quantify Vegetation Structure and Patch-Scale Vegetation and Ground Cover
Applied commonly used line-point intercept (LPI) and soil sampling methods to quantify vegetation and ground cover conditions and soil properties:
Hillslope-Scale LPI Plots
Hillslope Scale - 33 m x 30 m plots; n = 3 per treatment
Figure 10. Hillslope-scale LPI plot - Woodland
Figure 11. Hillslope-scale LPI Plot - sagebrush

## Slide 9: Methods: Quantify Vegetation Structure and Patch-Scale Vegetation and Ground Cover
Applied commonly used line-point intercept (LPI) and soil sampling methods to quantify vegetation and ground cover conditions and soil properties:
Patch-Scale LPI Plots
Patch Scale – 6 m x 2 m plots; n = 6 per microsite
Figure 12. Patch-scale LPI Plot - Sagebrush
Figure 13. Patch-scale LPI Plot – Tree canopy
Figure 14. Patch-scale LPI Plot - Intercanopy
Figure 15. Soil Cores (0-5 cm) For Texture

## Slide 10: Methods: RHEM Patch-Scale Runoff and Sediment Yield Modeling
RHEM used to predict runoff and sediment yield for each patch-scale plot.
RHEM requires the following user inputs:
User-specified scenario ID
User selected climate station from an internal list
soil texture class
slope angle and shape
cover characteristics.
https://apps.tucson.ars.ag.gov/rhem/tool

## Slide 11: Methods: RHEM Patch-Scale Runoff and Sediment Yield Modeling
RHEM applied for runoff and sediment yield prediction for each patch-scale plot using:
Representative climate station
Field-measured soil texture – loamy sand
Field-measured plot slope angle and shape
Field-measured (LPI) foliar and ground covers
https://apps.tucson.ars.ag.gov/rhem/tool

## Slide 12: Methods: RHEM Hillslope-Scale Runoff and Sediment Yield Modelling
Mean of all patch-scale intercanopy woodland runs (n= 6) x fractional intercanopy area (woodland intercanopy area, 68%)
Williams et al. 2022 –
Ecosphere 13:e4145
Figure 12. Sagebrush Hillslopes
For Sagebrush, hillslope-scale runoff and sediment yield estimated as mean of all sagebrush patch-scale model runs (n = 6).
Using methods from Williams et al. 2022, Woodland hillslope-scale runoff and sediment yield were determined as:
Mean of all patch-scale tree canopy woodland runs (n= 6) x fractional tree canopy cover (woodland area covered by trees, 32%)
Figure 13 & 14 Woodland Hillslopes – Area weighted based Tree Canopy & Intercanopy Area

## Slide 13: Results: Woodland Encroachment Impacts on Vegetation Structure and Canopy and Ground Cover
Site characterization = hillslope 33 m x 30 me plots
Figure 13. Plot L13 – Interspace
Coarse scale
2 m x 6 m plots
Average Bare ground cover Sagebrush Characterization site: 36.1 %
Average crust cover: 13.8%
Figure 17. Woodland Characterization site
Figure 16. Sagebrush Characterization site
Average Bare ground cover in woodland for site characterization plots: 36.5 %
Average crust cover: 22.8%
Bareground cover: 33.3%
Crust cover: 59.4%

## Slide 14: Results: Woodland Encroachment Impacts on Vegetation Structure and Canopy and Ground Cover
Site Characterization Plot
Coarse Scale
Site Characterization Plot
Woodland encroachment negatively impacts cover and increases bare ground
Graph 1. Basal Cover
Graph 2. Crust and bare ground cover
Graph 3. Ground Bare soil crust on course scale

## Slide 15: Results: Woodland Encroachment Impacts on Runoff and Sediment Yield
Runoff
(Graph 4 & 5)
  little difference between sagebrush and woodland
  weighted – tree microsites are stable
Sediment Yield
(Graph 6 & 7)
  noticeable difference especially in inter-canopy areas.
Chart: Runoff 25 Year Return Interval (mm)
| Sage | Intercanopy | Tree | Woodland Weighted
Runoff_25Yr_mm | 3.2632 | 4.9382 | 0.82517 | 3.622
Chart: Sediment Yield 25 Year Return Interval (Mg/ha)
| Sage | Intercanopy | Tree | Woodland Weighted
Runoff_25Yr_mm | 0.155 | 0.705 | 0.0555 | 0.49716
Chart: Runoff 100 Year Return Interval (mm)
| Sage | Intercanopy | Tree | Woodland Weighted
Runoff_25Yr_mm | 11.3042 | 14.1142 | 8.183 | 12.2162
Chart: Sediment Yield 100 Year Return Interval (Mg/ha)
| Sage | Intercanopy | Tree | Woodland Weighted
Runoff_25Yr_mm | 0.365 | 1.5132 | 0.2265 | 1.1014
Graph 4. Runoff RHEM Results for 25-year return interval
Graph 5. Runoff RHEM Results for 100-year return interval
Graph 6. Sediment RHEM Results for 25-year return interval
Graph 7. Sediment RHEM Results for 100-year return interval

## Slide 16: Results: Woodland Encroachment Impacts on Runoff and Sediment Yield
Crust cover is crucial to preventing erosion in the woodland
Woodland is less resilient than the sagebrush site regarding surface disturbance
Graph 8. Sediment yield 25-year return interval of crust cover.
Darker color = no crust
Lighter color = crust

## Slide 17: Conclusions
The sagebrush site generally provides greater utility (better provision of ecosystem services) in terms of sage grouse habitat, forage for wild/domestic grazing, resilience to disturbance
sagebrush site is more stable in terms of hydrologic function and erosion prevention.

## Slide 18: Acknowledgements
Jason Williams, Arizona Space Grant Consortium Research Mentor
Erin Phelps, Arizona Space Grant Consortium Grad Student Mentor
Michelle Coe, University of Arizona - Arizona Space Grant Consortium Manager
Dr. Chandra Holifield Collins, University of Arizona - Arizona Space Grant Consortium Program Manager
Jacob Blais, Arizona Space Grant Consortium Undergraduate Intern Advisor
Arizona Space Grant Consortium fellow interns

## Slide 19: Thank you!
Trisha Jean Lane
ttso@arizona.edu