## Slide 1: Design and Implementation of a Focused Laser Differential Interferometer for Hypersonic Boundary Layer Transition Measurements
Jackson Barger
Mentored by Dr. Alex Craig and John Flood
University of Arizona

## Slide 2: Boundary Layer Transition
Laminar vs Turbulent Boundary Layers
  Flow Instabilities
Thermal heating and Shear Forces
  Structural failure
Hypersonic Flight (M>5)
Mach 5 Ludwieg Tube (LT5)
Flood, J. et al (2023)
Grasacoustics.com

## Slide 3: Focused Laser Differential Interferometry (FLDI)
FLDI is a non-intrusive laser-based optical measurement system
Insensitive to density gradients outside the focused region
Expand, Polarize, Split, Focus
Can calculate density gradients to categorize flow instabilities
  Phase difference between signals
  Gladstone-Dale Relationship
Schmidt, Applied Optics 2015

## Slide 4: Design
Thin Lens Equation and Lens Geometry
  Lens Spacing
Physical Tunnel Constraints
Parts
  100mW 532nm Laser, -6mm focal length plano-concave lens, linear polarizer, 2-arcminute Wollaston Prism, 300mm focal length achromatic lens
d1
d2
Thin Lens Equation

## Slide 5: Benchtop Testing
Built, calibrated, and validated on benchtop
Nitrogen jet
  Changed Reynold’s number of a nitrogen jet to observe laminar to turbulent jet transition

## Slide 6: Wind Tunnel Testing
Hypersonic wind tunnel test at Mach 5
  7-degree cone with sharp tip
Measured boundary layer spectra

## Slide 7: Conclusions and Future Applications
Developed cutting-edge diagnostic for BLST lab
Successfully measured laminar-turbulent jet transition and measured boundary layer in wind tunnel test
Investigate Two Point and Multi-Point FLDI
Integrate with Schlieren
Bathel et al 2021
Davenport et al 2023

## Slide 8: Acknowledgements
NASA Space Grant
My mentor, Dr. Alex Craig and everyone else in the Boundary-Layer Stability and Transition Laboratory
Office of Naval Research

## Slide 9: Thank You