## Slide 1: NASA Arizona Space Grant Symposium 2025
Casa Grande Union High School Near Space Research Team

## Slide 2: ASCEND! Aerospace STEM Challenges to Educate New Discoverers
University of Arizona
Arizona State University
Embry-Riddle Aeronautical University
Arizona Western College
Glendale Community College
Pima Community College
Central Arizona College (Signal Peak)
Phoenix College
and Casa Grande Union High School
ASCEND!" (Aerospace STEM Challenges to Educate New Discoverers) is an Arizona Space Grant Consortium statewide Workforce Development program designed to involve undergraduate students from across Arizona in the full "design-build-fly-operate-analyze" cycle of a space mission.

## Slide 3: CGUHS Near Space Research Team
Project Manager
Landri Howard
Prototype Development
Hailianna Rodgers
Peyton Posey
Control System
Emily Geen
Enclosure
Zacheriah Buchanan
Aliceanna Villanueva
Axel Carrera
Documentarian
Rayne Tarman

## Slide 4: Mission Statement
The CGUHS Near Space Research Team will design, construct, test, and fly a high-altitude balloon payload to gather atmospheric data and 4K video during the flight.

## Slide 5: CGUHS Near Space Research Team ASCEND Project Roadmap
Phase I: Single Payload Atmospheric Data Collection and Imaging
Goal: Successfully launch and recover a single payload, collecting atmospheric data and capturing high-resolution imagery.
Timeline: Fall 2024, 2-3 months (COMPLETED)

## Slide 6: CGUHS Near Space Research Team ASCEND Project Roadmap
Phase II: Dual Payload RF Communication
Goal: Establish two-way RF communication between two payloads, transmitting internal payload temperature data.
Timeline: Spring 2025, 3-4 months

## Slide 7: CGUHS Near Space Research Team ASCEND Project Roadmap
Phase III: Air-to-Ground Mesh Network Prototyping
Goal: Establish a mesh network between a balloon payload and three ground-based autonomous rovers.
Timeline: Fall 2025, 4-6 months

## Slide 8: CGUHS Near Space Research Team ASCEND Project Roadmap
Phase IV: Multi-Balloon and Ground Rover Mesh Network
Goal: Expand the mesh network to include two balloon payloads and ground rovers.
Timeline: Spring 2026, 3-4 months

## Slide 9: Prototype Development
Hailianna Rodgers
Peyton Posey

## Slide 10: Prototype Development

## Slide 11: Endurance Testing

## Slide 12: Enclosure
Axel Carrera
Zacheria Buchanan
Aliceanna Villanueva

## Slide 13: Enclosure
Requirements
Development
Testing

## Slide 14
Original CUBESAT Idea
Transition to the ABS box
How the CAD was made

## Slide 15: Control System
Hailianna Rodgers
Peyton Posey

## Slide 16
Code Schematic

## Slide 17: Electrical
Emily Geen

## Slide 18: Power Distribution System

## Slide 19: Custom Printed Circuit Board

## Slide 20: Sensors and Electrical Components
Arduino Uno
NRF24L01
SD Card Reader
BME280
GUVA-S12SD UV Sensor
TMP36

## Slide 21: ASCEND Flight 51 November 24, 2024
Flight Distance 98 km (61 miles)
Landing at 32° 52.256'N, 111° 16.351'W, or 29 km (18 miles) northeast of the town of Eloy, Arizona near Highway AZ-79.
Burst occurred after 62 minutes with a total flight time of 94 minutes.
Payload mass of 8.7 kg (19.2 lbs),
Neck lift of 12.1 kg (26.5 lbs),
Ascent rate of 7.88 m/sec (1551 fpm)
Burst altitude of 29,656 meters (97,300 feet).
Descent rate at landing of 6.8 m/sec (1339 fpm)

## Slide 23: Launch

## Slide 24: Landing Site – Fall 2024

## Slide 25: Pre-Launch Briefing

## Slide 26: ASCEND Fight 55 March 29, 2025
Flight Distance 99.1 km (61.6 miles)
Landing at 32.78597,-111.22348, or 17.8 miles SE of Florence, AZ.
Burst occured after 63 minutes with a total flight time of 94 minutes.
Payload mass of 8.278 kg (18.251 lbs),
neck lift of 11.59 kg (25.49 lbs),
Ascent rate of 7.68 m/sec (1511 fpm)
Burst altitude of 29,869 meters (98,000 feet)
Descent rate at landing of 6.81 m/sec (1340 fpm)

## Slide 27: Landing Site – Spring 2025
By the time we had arrived at Oracle, burst had occurred, and the balloon payload was descending.
We rallied at the Circle K in Mammoth, and by that time the telemetry showed that the payload had landed at an altitude of about 6100 feet near Klondike.
Since Klondike is a ghost town with no maintained roads and it was by this time 3 pm, it was decided that one of the vehicles with off road ability would make the payload retrieval.
The rest of us headed for home.

## Slide 29: Future Work
Given the unsuccessful completion of Phase I and Phase II, the immediate future plans for this project must focus on a thorough failure analysis and a revised, more incremental approach. The primary goal shifts from rapid advancement to establishing a solid foundation of basic functionality.
Immediate Next Steps:
Comprehensive Failure Analysis
Focused Re-evaluation of Phase I
Iterative RF Communication Testing
Prioritize Reliability over Complexity
Staged Integration
Documentation and Knowledge Sharing

## Slide 30: Acknowledgements
Michelle Coe
Manager,
Arizona/NASA Space Grant Program
University of Arizona
Clayton G. Jacobs, KJ6QJS
President, Arizona Near Space Research www.ansr.org
Stephen Thomas, KE7TLS
Vice President,
Arizona Near Space Research
Shirley Campbell
Assistant Director
National Space Grant Foundation
John Morris
Certified Educator
Engineering | Software and App Design

## Slide 31
Thank you!

## Slide 32: Questions?